## Slide 1
UNIFIED ROBOT CONTROL INTERFACE
A common GUI and integration framework for agentic planning, Isaac ROS execution, and Picker2 learned skills
AGENTIC
ROS 2
RL SKILLS
Architecture proposal • grounded in the current repositories
PLAN
PERCEIVE
ACT
VERIFY

## Slide 2
INTERFACE EXAMPLE
CaP-X simulation: workflow and 3D visualization
02
Screenshot captured from the local Franka cube-lifting demonstration
Executable workflow • task events • MuJoCo view • interactive Viser scene

## Slide 3
GUI STRUCTURE
How the CaP-X GUI exposes robot execution
03
Reference: local CaP-X Franka cube-lifting demonstration
1 Pseudo-code interface
High-level, readable robot workflow. • Object pose / grasp pose • Motion planning • Robot and gripper commands • Execution result
WORKFLOW
2 YAML task configuration
Reproducible task setup. • Robot and simulator • APIs and task prompt • Model / workflow • Visualization and outputs
CONFIG
3 3D visualization
Live execution context. • Robot and object state • Camera view and frames • Grasps and trajectories • Interactive inspection
VISER
Task YAML → high-level Python workflow → perception / planning / motion services → live 3D evidence

## Slide 4
MODULE VIEW
Agentic robot APIs and current implementations
04
Sources: agentic_robots/apis · agentic_robots/services · Isaac ROS manipulation workflow
Task intent
CodeAgent
Allowlisted runtime
Robot capabilities
Robot Control API
Interface • pose and robot state • Cartesian/joint motion • gripper open/close Current implementation • ActionApi • FrankaReal + libfranka bridge • FrankaSim / PyBullet
Perception API
Interface • object segmentation and pose • point-cloud extraction • grasp candidates Current implementation • SAM3 segmentation service • Contact-GraspNet grasp service • Fundation Pose Estimation
• calibrated D455 observations
Planning API
Interface • IK and target-pose planning • collision-aware trajectory • execute / cancel / report Current implementation • PyRoKi motion service (experimental) • cuMotion + nvblox available in Isaac ROS
Current path: SAM3 → mask • GraspNet → grasp • PyRoKi / cuMotion → trajectory • robot backend → motion