## Slide 1
UNIFIED ROBOT CONTROL INTERFACE
A common GUI and integration framework for agentic planning, Isaac ROS execution, and Picker2 learned skills
AGENTIC
ROS 2
RL SKILLS
Architecture proposal • grounded in the current repositories
PLAN
PERCEIVE
ACT
VERIFY

## Slide 2
INTERFACE EXAMPLE
CaP-X simulation: workflow and 3D visualization
02
Screenshot captured from the local Franka cube-lifting demonstration
Executable workflow • task events • MuJoCo view • interactive Viser scene

## Slide 3
GUI STRUCTURE
How the CaP-X GUI exposes robot execution
03
Reference: local CaP-X Franka cube-lifting demonstration
1 Pseudo-code interface
High-level, readable robot workflow. • Object pose / grasp pose • Motion planning • Robot and gripper commands • Execution result
WORKFLOW
2 YAML task configuration
Reproducible task setup. • Robot and simulator • APIs and task prompt • Model / workflow • Visualization and outputs
CONFIG
3 3D visualization
Live execution context. • Robot and object state • Camera view and frames • Grasps and trajectories • Interactive inspection
VISER
Task YAML → high-level Python workflow → perception / planning / motion services → live 3D evidence

## Slide 4
MODULE VIEW
Agentic robot APIs and current implementations
04
Sources: agentic_robots/apis · agentic_robots/services · Isaac ROS manipulation workflow
Task intent
CodeAgent
Allowlisted runtime
Robot capabilities
Robot Control API
Interface • pose and robot state • Cartesian/joint motion • gripper open/close Current implementation • ActionApi • FrankaReal + libfranka bridge • FrankaSim / PyBullet
Perception API
Interface • object segmentation and pose • point-cloud extraction • grasp candidates Current implementation • SAM3 segmentation service • Contact-GraspNet grasp service • Fundation Pose Estimation
• calibrated D455 observations
Planning API
Interface • IK and target-pose planning • collision-aware trajectory • execute / cancel / report Current implementation • PyRoKi motion service (experimental) • cuMotion + nvblox available in Isaac ROS
Current path: SAM3 → mask • GraspNet → grasp • PyRoKi / cuMotion → trajectory • robot backend → motion

## Slide 5
PICKER2 LEARNING ROADMAP
From Genesis simulation to the cargo robot
05
Four validation gates; each stage preserves physical contact and measurable task success
1
SIMULATION SETUP
Robot + D455 + hook fingertips Two 4 kg suitcase proxies Cargo platform and 8×8 scene
→
2
STATE-BASED RL
Privileged geometry + proprioception Reach → grasp → lift → rotate Place → release → retreat
→
3
STATE + RGB-D
Wrist D455 RGB and depth Visual encoder + robot state Distill from state-based teacher
→
4
REAL ROBOT
Calibration and safety limits Domain randomization Slow staged deployment
Final objective: start at home, physically grasp the handle, load flat with handle toward +X, release, and return safe.

## Slide 6
1 · SIMULATION SETUP
One Genesis scene, realistic Picker2 contacts
06
Assets are generated from the Picker2 ROS description; luggage visuals are aligned to collision geometry
SINGLE ENVIRONMENT
8 × 8 TRAINING
Stationary Picker2 base • D455 at the wrist • customized 2FG14 retaining fingertips
Training Environments
Physics: 4 kg luggage · primitive contact proxies · no fixed grasp constraint · bilateral fingertip contact

## Slide 7
2 · STATE-BASED RL
Actions, observations, rewards, and curriculum
07
PPO first learns with privileged state; success is determined by physical luggage state—not trajectory completion
ACTION · 7D
• Δx, Δy, Δz
• Δroll, Δpitch, Δyaw
• normalized gripper command
• bounded at every control step
OBSERVATION · 63D
• 46D robot/luggage state
• phase target Δposition + quaternion
• 9D task-phase one-hot + age
• TCP, handle, target and velocities
REWARD + TERMINATION
• target-distance progress
• bilateral contact and retention
• lift, flatness, target pose, +X handle
• release, retreat, success / timeout
Current engineering status: residual-RL bootstrap reaches grasp/lift/transport; rotation and pure end-to-end RL remain open milestones.
PPO RSL-RL

## Slide 8
3 · ROBOT STATE + IMAGE
Transition from privileged state to wrist RGB-D
08
Keep proprioception; replace privileged object pose with learned visual features
D455 INPUT
RGB frame Depth / point cloud Camera intrinsics Wrist extrinsics
VISUAL ENCODER
Compact CNN / ViT Depth-aware fusion Handle + luggage geometry Temporal features
POLICY FUSION
Visual latent Joint + gripper state TCP velocity Previous action
7D CONTROL
Cartesian delta Orientation delta Gripper command Phase / memory
→
→
→
Training recipe: state-policy teacher → synchronized RGB-D rollouts → behavior distillation → PPO fine-tuning with visual randomization.

## Slide 9
SIMULATION EVIDENCE
Current Picker2 Manual Process
10
Embedded 35-second recording from the local Genesis environment (click Play in presentation mode)
WHAT TO WATCH
• home-position start
• handle approach
• physical grasp
• retained lift
• transport toward platform
• current rotation